## Slide 1
www.forensicstats.org
Stephanie Reinders, PhD. Candidate, Mathematics Dept, Iowa State University
Li Lin, PhD. Candidate, Mathematics Dept, Iowa State University
Wenhao Chen, PhD. Candidate, Electrical and Computer Engineering Dept, Iowa State University
Dr. Yong Guan, Professor, Electrical and Computer Engineering Dept, Iowa State University
Dr. Jennifer Newman, Associate Professor, Mathematics Dept, Iowa State University
Electronic Imaging 2020
Score-based likelihood ratios
for camera device identification

## Slide 2: The camera device identification problem
A type of specific source identification problem
Scenario:
  Evidence
    Unknown source evidence - Digital image from an unknown camera device (source) is recovered as evidence in a crime
    Specific known source evidence - A camera fingerprint is estimated from a suspect’s camera device (source)
  The prosecution wants to determine whether image and camera fingerprint originate from the same specific camera device (the suspect’s camera device)
  Assumption: the prosecution has access to the suspect’s camera and is able to take images on it to be used in analysis

## Slide 3: The camera device identification problem
The prosecution and defense hypotheses:
  image and camera fingerprint originate from the same specific camera device
  image and camera fingerprint do not originate from the same specific camera device
The end goal is to determine whether the evidence supports or
Terminology
  Match – an image and a camera fingerprint originate from the same camera device
  Non-match – an image and a camera fingerprint no not originate from the same camera device
Notes: These are the hypotheses commonly used for SLRs in other forensic areas
Prior work in device identification labels the first hypothesis as H_1 and the second as H_0

## Slide 4: Score-based likelihood ratios (SLR)
Quantify the weight of forensic evidence
  Describe the strength of evidence in favor of match or non-match, giving stakeholders more information than a binary decision of match or non-match
Implemented in handwriting1, shoeprint2, and glass evidence2
Limited implementation in camera device identifcation3,4

## Slide 5: Score-based likelihood ratios v. Likelihood Ratios
Score-based likelihood ratios
Model similarity scores applied to features
Likelihood ratios
Directly model features
SLRs and LRs have different statistical properties!1

## Slide 6: Score-based likelihood ratios (SLR)
The SLR measures the relative probability of obtaining the similarity score if the image and camera fingerprint originate from the same specific camera device
there are 3 ways to define this1

## Slide 7: Three methods for defining and calculating non-matches
Source-anchored (fix specific device
  Calculate scores between camera fingerprints from and images from other devices
Trace-anchored (fix specific image
  Calculate scores between the image and camera fingerprints of devices other than specific device
General match (don’t fix or )
  Calculate scores between an image from a randomly selected camera other than and the camera fingerprint of a second camera other than
Each method may result in a different distribution

## Slide 8: Definitions of non-matches used in prior device id work
Source-anchored
Lukas, Fridrich, and Goljan 2005
Chen, Fridrich, and Goljan 2007
Chen et. al. 2008
Hu, Yu, and Jian 2009
Nordgaard and Hoglund 2011
van Houten et. al. 2011
Costa et. al. 2012
Goljan and Fridrich 2012
Trace-anchored
Lukas, Fridrich, and Goljan 2005
General Match
Goljan, Fridrich, and Filler 2009

## Slide 9: Definitions of non-matches used in prior device id work
Source-anchored
Lukas, Fridrich, and Goljan 2005
Chen, Fridrich, and Goljan 2007
Chen et. al. 2008
Hu, Yu, and Jian 2009
Nordgaard and Hoglund 2011
van Houten et. al. 2011
Costa et. al. 2012
Goljan and Fridrich 2012
Trace-anchored
Lukas, Fridrich, and Goljan 2005
We use this method
General Match
Goljan, Fridrich, and Filler 2009

## Slide 10: Prior work with SLRs in device identification
Nordgaard and Höglund1
  Introduced SLRs for camera device identification
  Only considered two devices
  Only implemented the source-anchored definition of non-matches
van Houten, Alberink and Geradts2
  Expanded Nordgaard and Höglund’s results to more devices
  Only implemented the source-anchored definition of non-matches
Our research
  Current work - Implement trace-anchored SLRs in device id for the first time
  Future work – compare results of all three methods in SLRs

## Slide 11: Comparing SLR approach and previous approach to camera device identification
Universal Detector
Most widely used approach to camera device identification
The goal is to develop a statistically sound, relevant set of scores that can be applied to any image and device
If or changes, a new set of scores does not need to be generated
Outcome: Binary decision
Score-based likelihood ratios
The goal is to create statistically sound, relevant sets of matching and non-matching scores specific to image and camera fingerprint
If or changes, a new relevant set of scores is generated
Outcome: Quantification of the weight of evidence – A real number greater than or equal to zero

## Slide 12: Comparing SLR approach and previous approach to camera device identification
Universal detector
Use Photo-Response Non-Uniformity (PRNU) as a camera fingerprint
Use a similarity score
Compute the score between the image and camera fingerprint
Score-based likelihood ratios
Use Photo-Response Non-Uniformity (PRNU) as a camera fingerprint
Use a similarity score
Evaluate probability density functions fit to a sets of matching and non-matching scores at Quantify the weight of evidence in favor of a match or non-match

## Slide 13: Photo Response Non-Uniformity (PRNU)
Used as a camera fingerprint1
Result of sensor imperfections
Estimated from flat-field or natural images with a denoising filter1, 2
In the camera device identification problem
  Estimate the noise residual of questioned image
  Estimate the PRNU or camera fingerprint of specific known device

## Slide 14: Similarity scores
In the universal detector approach
  Normalized correlation used in earlier works1
  Peak-to-Correlation Energy (PCE) replaced normalized correlation2
    If using PCE, the decision threshold does not need to be adjusted if a periodic component such as linear pattern is present
    If using PCE, the decision threshold does not need to be recalculated if the image size changes

## Slide 15: Similarity scores
In the SLR approach
  We use the score (One minus the normalized correlation)
  Reason: Normalized correlation has much smaller variance than Peak to Correlation Energy (PCE), so it produces fewer ‘inconclusive’ instances where the SLR denominator is zero and the SLR numerator is tiny than PCE (more about this later)
  Justification: Because the SLR approach does not use a decision threshold, the problems normalized correlation encounters in the universal detector approach are not problems for SLR

## Slide 16: Generate two sets of scores
Matching scores
Scores between the noise residual of an image and the camera fingerprint of its source device
Non-matching scores
Scores between the noise residual of an image and the camera fingerprint of another device
Example data
Suppose matching scores follow a normal distribution and non-matching scores follow a normal distribution
Histograms of 300 randomly generated matching and non-matching scores
Example using idealized data

## Slide 17: Fit pdfs to both sets of scores
Example
Fit a normal probability density function to each set of scores
Normal pdfs fit to the matching and non-matching scores

## Slide 18: Universal Detector Set Threshold
Choose decision threshold
Typically chosen to produce a specific false acceptance rate
Example
yields a false acceptance rate of 0.01
The decision threshold and normal pdfs fit to the matching and non-matching scores

## Slide 19: Universal Detector Set Threshold
Choose decision threshold
Typically chosen to produce a specific false acceptance rate
Example
yields a false acceptance rate of 0.01
The decision threshold and normal pdfs fit to the matching and non-matching scores

## Slide 20: Universal Detector Make decision
Calculate the score between the questioned image and the suspect’s camera
If conclude non-match
If conclude match
The score is compared to the decision threshold

## Slide 21: SLR
Normal pdfs fit to the matching and non-matching scores

## Slide 22: SLR Evaluate pdfs at score
Calculate the score between the questioned image and the suspect’s camera
Evaluate
Normal pdfs fit to the matching and non-matching scores

## Slide 23: SLR Evaluate pdfs at score
Calculate the score between the questioned image and the suspect’s camera
Evaluate
Evaluate
Normal pdfs fit to the matching and non-matching scores

## Slide 24: SLR Compute the SLR
Example
SLR = 12.47
The likelihood that and originated from the same device is 12.47 times larger than the likelihood that they don’t both originate from device
Normal pdfs fit to the matching and non-matching scores

## Slide 25: Experiments
10,000 images from BOSSbase image dataset
7 digital still camera devices
The original images were taken in the native camera formats
We processed the images:
  Converted images to TIFF in Photoshop
  Center-cropped to 512 x 512 and saved as PNG in Matlab
We used the PRNU extraction code created by DDE Labs
  http://dde.binghamton.edu/download/camera_fingerprint/
  (Thanks DDE labs!)

## Slide 26: Experiment settings
We estimated each PRNU camera fingerprint from 50 randomly selected images
We used the similarity score
We calculated non-matches using the trace-anchored method
We used kernel density estimation to fit probability density functions and to matching scores and non-matching scores

## Slide 27: Assumptions
All images are the same size
Images have not been resized, compressed, or transformed in other ways

## Slide 28: Algorithm
Boxplots of SLR values. Questioned images are from Canon EOS 7D
For each questioned image Canon EOS 7D
For each BOSSbase device
  Compute camera fingerprint from
  Calculate

## Slide 29: Experiments
Boxplots of SLR values. Questioned images are from Canon Rebel XSi
For each questioned image Canon Rebel XSi
For each BOSSbase device
  Compute camera fingerprint from
  Calculate

## Slide 30: Experiments
Boxplots of SLR values. Questioned images are from Pentex K20D
For each questioned image Pentex K20D
For each BOSSbase For each BOSSbase device
  Compute camera fingerprint from
  Calculate

## Slide 31: Experiments
Boxplots of SLR values. Questioned images are from Nikon D70
For each questioned image Nikon D70
For each BOSSbase device
  Compute camera fingerprint from
  Calculate

## Slide 32: Experiments
Boxplots of SLR values. Questioned images are from Leica M9
For each questioned image Leica M9
For each BOSSbase device
  Compute camera fingerprint from
  Calculate

## Slide 33: Experiments
For each questioned image Canon EOS 400D
For each BOSSbase device
  Compute camera fingerprint from
  Calculate
Boxplots of SLR values. Questioned images are from Canon EOS 400D

## Slide 34: Experiments
Boxplots of SLR values. Questioned images are from Canon EOS 40D
For each questioned image Canon EOS 40D
For each BOSSbase device
  Compute camera fingerprint from
  Calculate

## Slide 35: Summary and conclusions
SLR provides a quantification of the weight of evidence
SLR correctly returns high values for true matches (an image and the device it came from) for all 7 devices
SLR incorrectly returns high values for images from Canon EOS 400D or Canon EOS 40D when compared to the other device

## Slide 36: Future work
Identify the cause of misleading SLR values for the Canon EOS 400D and Canon EOS 40D
Compare source-anchored, trace-anchored and general match SLRs for camera device identification
Extend results to more camera devices using other image datasets
  ALASKA
  StegoAppDB
Extend results to different sized images and image that have been resized or compressed

## Slide 37: Acknowledgements
This work was partially funded by the Center for Statistics and Applications in Forensic Evidence (CSAFE) through Cooperative Agreement #70NANB15H176 between NIST and Iowa State University, which includes activities carried out at Carnegie Mellon University, University of California Irvine, and University of Virginia.

## Slide 38: Maximum SLR
We calculated the SLR for questioned image and each specific device
  Each image has 7 SLR values, one for each device
For each image we find the device that produces the maximum SLR for

## Slide 39: Maximum SLR
 |  | Specific Known Device |  |  |  |  |  | 
 |  | Canon EOS 400D | Canon EOS 40D | Canon EOS 7D | Canon Rebel XSi | Pentex K20D | Nikon D70 | Leica M9
Questioned Image | Canon EOS 400D | 92.47% | 7.46% | 0% | 0% | 0% | 0.07% | 0%
 | Canon EOS 40D | 31.45% | 67.21% | 0% | 1.64% | 0% | 0% | 0%
 | Canon EOS 7D | 0% | 0% | 100% | 0% | 0% | 0% | 0%
 | Canon Rebel XSi | 0.13% | 0% | 0% | 99.74% | 0% | 0% | 0.13%
 | Pentex K20D | 0% | 0% | 0.14% | 0.14% | 97.05% | 0.07% | 0.07%
 | Nikon D70 | 0% | 0% | 0% | 0% | 0% | 100% | 0%
 | Leica M9 | 0% | 0% | 0% | 0.07% | 0% | 0.37% | 99.56%
 |  | Canon EOS 400D | Canon EOS 40D | Canon EOS 7D | Canon Rebel XSi | Pentex K20D | Nikon D70 | Leica M9
 | Canon EOS 400D | 92.47% | 7.46% | 0% | 0% | 0% | 0.07% | 0%
 | Canon EOS 40D | 31.45% | 67.21% | 0% | 1.64% | 0% | 0% | 0%
 | Canon EOS 7D | 0% | 0% | 100% | 0% | 0% | 0% | 0%
 | Canon Rebel XSi | 0.13% | 0% | 0% | 99.74% | 0% | 0% | 0.13%
 | Pentex K20D | 0% | 0% | 0.14% | 0.14% | 97.05% | 0.07% | 0.07%
 | Nikon D70 | 0% | 0% | 0% | 0% | 0% | 100% | 0%
 | Leica M9 | 0% | 0% | 0% | 0.07% | 0% | 0.37% | 99.56%
For 92.47% of the images from Canon EOS 400D, the highest SLR value occurred when Canon EOS 400D was set as the specific known device